## Slide 1: Security in Automobiles: Vulnerability and Protection (OBD-II Access Control)
Master Thesis. Michiel Willems, 25/04/18

## Slide 2: Outline
Introduction
OBD-II Access Control
Paper: Security, Vulnerability and Protection of Vehicular On-board Diagnostics
  Introduction
  Proposed Security Solutions
Current Thesis Status
Planning next two months

## Slide 3: Introduction

## Slide 4: Introduction
Automobile hacking has become one of the major concerns for software security today:
  Over 100M lines of code deployed over more than 70 ECU’s.
  Networking protocols (e.g. CAN).
  Increasing connectability (Bluetooth, Wifi, etc).
Lee Pike, Jamey Sharp, Mark Tullsen, Patrick C. Hickey and James Bielman. 2015.
Securing the automobile: A comprehensive approach.
Dan Klinedinst, Christopher King. 2016
On Board Diagnostics: Risks and Vulnerabilities of the Connected Vehicle

## Slide 5: Introduction

## Slide 6: Introduction

## Slide 7: Introduction
On Board Diagnostics Protocol.
  Help Technicians Diagnose and Repair Complex Problems
  Allows access to vehicle subsystems via connector.
  Introduces parameter ID’s (PID) to request data from ECU’s.
  PID manufacturer and model specific.
  Works with multiple signalling protocols, but CAN mostly used.
https://en.wikipedia.org/wiki/On-board_diagnostics
Allen Lyons, California Air Resources Board , On-Board Diagnostics (OBD) Program Overview, 2015 .

## Slide 8: OBD-II
Vehicle Network

## Slide 9: Security Issues
’CAN, by design, offers no protection from manipulation’
(Miller, 2013), (Koscher, 2010)
No source address => No certainty about origin.
Broadcast nature => Information Disclosure.
Prioritized ID’s => Denial of Service.
No support for encryption or authentication.

## Slide 10: Threat Model
Vehicle Network
Physical Access to OBD-II DLC.
Ability to inject arbitrary packets.
Able to exploit vulnerabilities in ECU software.

## Slide 11: OBD-II Access Control

## Slide 12: Introduction
Thesis Subject: Role Based Access Control.
Every role determines what kind of access is permitted.
For example:
  Repair shop => Read diagnostics information only.
  Official dealership => Diagnostics + ability to fix/test faulty ECU’s.
  Police => Check integrity of vehicle network.

## Slide 13: Introduction
Vehicle Network
Private Key
Public Key
Central Gateway

## Slide 14: Introduction
Challenges:
  PKI infrastructure.
  Authentication protocol (challenge response).
  Permissions table.
  Secure private key API.

## Slide 15: Security, Vulnerability and Protection of Vehicular On-board Diagnostics
Aastha Yadav, Gaurav Bose, Radhika Bhange, Karan Kapoor, N.Ch.S.N Iyengar, Ronnie D. Caytiles
VIT University.Vellore-632014, Tamilnadu, India, Hannam University, Korea

## Slide 16: Paper - Introduction
Outline:
  Introduction
  Motivation
  Background Research
  Points Entry
  On-Board Diagnostic (OBD)-II Port
  OBD-II Port Security Threats
  Security Solution
  Conclusion

## Slide 17: Paper - Introduction
Outline:
  Introduction
  Motivation
  Background Research
  Points Entry
  On-Board Diagnostic (OBD)-II Port
  OBD-II Port Security Threats
  Security Solution
  Conclusion

## Slide 18: Security, Vulnerability and Protection of Vehicular On-board Diagnostics
Aastha Yadav, Gaurav Bose, Radhika Bhange, Karan Kapoor, N.Ch.S.N Iyengar, Ronnie D. Caytiles
VIT University.Vellore-632014, Tamilnadu, India, Hannam University, Korea
Proposed Security Solutions

## Slide 19: Security Solutions – Seed Key Algorithm
Implement security at ECU level.
Every ECU holds a secret key.
Algorithm:
  Tester sends a PID to the ECU.
  ECU sends a seed value to the Tester.
  Both ECU and Tester calculate response from seed and secret key.
  Tester sends response to ECU where it is verified.

## Slide 20: Security Solutions – Seed Key Algorithm
Security Issues:
  Same secret key shared.
  Secret key stored in unprotected memory.
  Algorithms are proprietary and Confidential (Security through Obscurity).
  Seed values often too short ( 10 min to crack 16 bit seed ).
K. Koscher, A. Czeskis, F. Roesner, S. Patel, T. Kohno, S. Checkoway, D. McCoy, B. Kantor, D.Anderson and H.a.o. Shacham,
"Experimental security analysis of a modern automobile", Security and Privacy (SP), 2010 IEEE Symposium on, (2010).

## Slide 21: Security Solutions – Two Way Authentication
Extends Seed-Key Algorithm.
Introduce device that allows client (owner of car) to control access to the OBD-II port.
Device can be a pager, cell phone, smartphone app, bluetooth, etc.
Device allows client to receive and send acknowledgments.

## Slide 22: Security Solutions – Two Way Authentication

## Slide 23: Security Solutions – Timer Method
Extends Two-Way authentication method.
Introduces 2 things:
  Timer started once seed is received, if it runs out the client is notified.
  Client needs to enter code when completing acknowledgement.
Timer should prevent brute force attacks.

## Slide 24: Paper – My Issues
Solution assumes official tester device.
  Custom tester software could use revealed secret keys.
  Custom tester software would bypass two-way authentication.
Implementation uses small key and seed sizes.
  Demo uses 5 bit seeds and keys.
ECU is implemented only virtually (no CAN).

## Slide 25: Current Thesis Status

## Slide 26: Current Thesis Status
2 DVK90CAN1 AVR development boards (AT90CAN128).
Gateway:
  Holds public keys & permissions table.
Tester:
  Implements private key API.
  Authenticate & send OBD-II messages.

## Slide 27: Current Thesis Status
Authentication Request.
Tester
Gateway
Remote CAN frame
With Specific ID

## Slide 28: Current Thesis Status
Challenge
Tester
Gateway
2 CAN Frames
128 bit Challenge

## Slide 29: Current Thesis Status
Key Attestation
Tester
Gateway
8 CAN frames
512 bit Signature of Challenge

## Slide 30: Current Thesis Status
Elliptic Curve Digital Signature Algorithm.
Key Size:
  Security level is Key Size / 2 (smaller key than normal DSA).
  According to NSA 256 bit key sufficient (128-bit security level) .
Signature Size:
  Security level is Signature size / 4.
  A signature of size 512 bit will be sufficient (128-bit security level).
https://en.wikipedia.org/wiki/Key_size#cite_note-19
https://en.wikipedia.org/wiki/Elliptic_Curve_Digital_Signature_Algorithm

## Slide 31: Current Thesis Status
Authentication Request.
Tester
Gateway
Remote CAN frame
Acknowledgment

## Slide 32: Current Thesis Status
Send OBD-II message
Tester
Gateway
OBD-II message

## Slide 33: Current Thesis Status
Former protocol is for sending 1 OBD-II message.
If multiple messages are to be sent shared secret is established:
  Elliptic Curve Diffie-Hellman
Shared secret used as new symmetric key.
Every OBD-II message followed by MAC of message using shared symmetric key.
Periodically new symmetric key established.

## Slide 34: Current Thesis Status
Current Implementation:
  Relevant Microcontroller functions explored.
  2 AVR boards can send and receive CAN messages.
  Serial link between board and pc (for demo).
  Elliptic Curve Library (micro-ecc) imported and tested (Key Storage).
https://github.com/kmackay/micro-ecc

## Slide 35: Planning next 2 months

## Slide 36: Planning
Implementation:
  Finish Authentication + ECDH protocol.
  Build permissions table.
  Tester private key API.
    represents online API for interacting with private keys.
    This API should be secure!
Testing.

## Slide 37: Planning
Writing:
  Finishing touches: Literary Review, Background (CAN & OBD-II), Contributions, Introduction and Abstract.
  OBD-II Access control (explanation of implemented protocol).
  Formulation and interpretation of test results.
  Conclusion.

## Slide 38: Questions?

## Slide 39: OBD-II
On Board Diagnostics Protocol.
  Help Technicians Diagnose and Repair Complex Problems
  Allows access to vehicle subsystems via connector.
  Introduces parameter ID’s (PID) to request data from ECU’s.
  PID manufacturer and model specific.
  Works with multiple signalling protocols, but CAN mostly used.
https://en.wikipedia.org/wiki/On-board_diagnostics

## Slide 40: OBD-II
Vehicle Network

## Slide 41: OBD-II
Vehicle Network
OBD-II
Data Link Connector

## Slide 42: OBD-II
Vehicle Network
Diagnostic
Scan Tool

## Slide 43: OBD-II
  Scan Tools.

## Slide 44: OBD-II
Vehicle Network
CAN Bus

## Slide 45: CAN
Controller Area Network.
  Bus allowing communications between ECU’s inside the vehicle.
  Message Based Protocol (Frame).
  Carrier Sense Multiple Access with Collision Avoidance (CSMA/CA).
  Not only communications protocol implemented in vehicles (cf LIN, MOST) but most common.
https://en.wikipedia.org/wiki/CAN_bus

## Slide 46: OBD-II
Vehicle Network

## Slide 47: Security Issues

## Slide 48: Security Issues
’CAN, by design, offers no protection from manipulation’
(Miller, 2013), (Koscher, 2010)
No source address => No certainty about origin.
Broadcast nature => Information Disclosure.
Prioritized ID’s => Denial of Service.
No support for encryption or authentication.

## Slide 49: Security Issues
Potential hacking results.
  Vehicle Theft.
  Changing Emission information (“Dieselgate”).
  Reduce odometer value.
  Change recorded data after crash.
  …
EXTREMETECH, „Hack the diagnostics connector, steal yourself a BMW in 3 minutes
Stephanie Bayer, Thomas Enderle, Dennis Kengo Oka , Marko Wolf .
Security Crash Test – Practical Security Evaluations of Automotive Onboard IT Components

## Slide 50: Threat Model
Vehicle Network
Physical Access to OBD-II DLC.
Ability to inject arbitrary packets.
Able to exploit vulnerabilities in ECU software.
Enable wireless connectivity.

## Slide 51: Proposed Solution: OBD-II Role Based Access Control

## Slide 52: Solution
Proposed solution: Role Based Access Control.
Every role determines what kind of access is permitted.
For example:
  Repair shop => Read diagnostics information only.
  Official dealership => Diagnostics + ability to fix/test faulty ECU’s.
  Police => Check integrity of vehicle network.

## Slide 53: Solution
Central gateway (CGW).
  Acts as router for all subnetworks + gate for all incoming data.
Perfect place to implement access control solution.

## Slide 54: Solution
Vehicle Network
Private Key
Public Key
Central Gateway

## Slide 55: Solution
Implementation:
  Microcontroller with CAN controller (AT90CAN128).
  CAN Transceiver.
  OBD-II connector.
Demo:
  CAN testbench designed at KuLeuven for testing VulCAN.
Jo Van Bulck, Jan Tobias Mühlberg, and Frank Piessens
December 2017

## Slide 56: Planning Next Three Months

## Slide 57: Planning
December:
  Get Familiar with Microcontroller software development.
  Write December paper/poster.
January & February:
  Implement a simple CAN compliant device.
  Start Implementing rudimentary access control.

## Slide 58: Questions? Notes: - Timing.

## Slide 59
Timing difficulties.
Major Challenges!: Key infrastructure, Key size, …
No Slowing Down!!!

## Slide 60: CAN Protocol

## Slide 61: CAN
Controller Area Network.
  Bus allowing communications between ECU’s inside the vehicle.
  Message Based Protocol.
  Carrier Sense Multiple Access with Collision Avoidance (CSMA/CA).
  Not only communications protocol implemented in vehicles (cf LIN, MOST) but most common.

## Slide 62: CAN Frame
Identity Field
  Used to identify each ECU in the vehicle.
  Also specifies a priority (Lowest ID = highest priority).
  Bitwise contention resolution (1 = Recessive & 0 = Dominant).
Name | SOF | ID | RTR | IDE | r0 | DLC | Data | CRC | CRCd | ACK | EOF
No. Bits | 1 | 11 | 1 | 1 | 1 | 4 | 64 | 15 | 1 | 2 | 7

## Slide 63: CAN Bitwise Contention Resolution
1 | 1 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0
0 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0
Node 1
Node 2
Node 3
Node 4
Value Transmitted: 0

## Slide 64: CAN Bitwise Contention Resolution
1 | 1 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0
0 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0
Node 1
Node 2
Node 3
Node 4
Value Transmitted: 0

## Slide 65: CAN Bitwise Contention Resolution
1 | 1 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0
0 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0
Node 1
Node 2
Node 3
Node 4
Value Transmitted: 0

## Slide 66: CAN Bitwise Contention Resolution
1 | 1 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0
0 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0
Node 1
Node 2
Node 3
Node 4
Value Transmitted: 1

## Slide 67: CAN Frame
Data Field
  Carries the payload.
  Length is 64 so only 8 bytes of data in each message.
Name | SOF | ID | RTR | IDE | r0 | DLC | Data | CRC | CRCd | ACK | EOF
No. Bits | 1 | 11 | 1 | 1 | 1 | 4 | 64 | 15 | 1 | 2 | 7

## Slide 68: OBD-II

## Slide 69: OBD-II
Parameter ID’s (PID)
  Codes to request data from a vehicle.
  Typical Use (with scan tool connected to DLC):
    Technician enters PID on the scan tool.
    PID is sent to the CAN bus (accessed via the DLC).
    Some ECU recognises the PID and reports the corresponding value on the bus.
    Scan tool reads response and displays it to the technician.

## Slide 70: Security Issues
Potential hacking results (safety critical).
  Driver Distractions (wipers etc.).
  Engine shutoff.
  Steering changes.
  …

## Slide 71: Physical Access
Impossible to completely deny physical access.
Solutions rely on reducing potential harm of unauthorized access:
  Seed-key mechanism
  Two-way authentication between ECU’s.
  Timer method.
  Intrusion detection system.
  Honeypot.
  VulCAN.

## Slide 72: Bluetooth
Standard Bluetooth security not sufficient.
Large protocol stack, so susceptible to multiple attacks:
  Cipher attacks, Bluejacking, Backdoor attack, etc.
Solutions should apply to the Bluetooth implementation used inside the vehicle.

## Slide 73: Remote Keyless Entry
Most cars today use RF-based remote keyless entry (RKE)
radio transmitter sends encrypted data containing identifying information.
The ECU can determine if the key is valid and lock, unlock, and start the vehicle

## Slide 74: Tire Pressure Monitoring System
Each tire has pressure sensor.
Transmits real time data to an ECU.
Radio signal can be blocked/mimicked.
  Solution: ?

## Slide 75: Distributed Software

## Slide 76: Secure Software & Systems