## Slide 1: Security in Automobiles: Vulnerability and Protection (OBD-II Access Control)
Master Thesis. Michiel Willems, 06/12/17

## Slide 2: Outline
Introduction
Background
  OBD-II Protocol
  CAN Protocol
Security Issues
OBD-II Access Control
Planning next three months

## Slide 3: Introduction

## Slide 4: Introduction
Modern vehicle is a “Computer on Wheels”.
  Over 100M lines of code deployed over as many as 70 ECU’s.
  Networking protocols to facilitate internal communications (e.g. CAN).
  Increasing connectability (Bluetooth, Wifi, etc).
Lee Pike, Jamey Sharp, Mark Tullsen, Patrick C. Hickey and James Bielman. 2015.
Securing the automobile: A comprehensive approach.
Dan Klinedinst, Christopher King. 2016
On Board Diagnostics: Risks and Vulnerabilities of the Connected Vehicle

## Slide 5: Introduction
Aastha Yadav, Gaurav Bose, Radhika Bhange, Karan Kapoor, N.Ch.S.N Iyengar, Ronnie D. Caytiles. 2016.
Security, Vulnerability and Protection of Vehicular On-board Diagnostics

## Slide 6: Introduction
Goal of thesis: Securing the OBD-II port by implementing some kind of access control mechanism.
More Precisely:
  Role Based Access Control.

## Slide 7: OBD-II Protocol

## Slide 8: OBD-II
On Board Diagnostics Protocol.
  Allows access to vehicle subsystems via data link connector.
  Introduces parameter ID’s (PID) to request data from ECU’s.
  PID specifications are manufacturer and model specific.
  Works with multiple signalling protocols, but CAN mostly used.
https://en.wikipedia.org/wiki/On-board_diagnostics

## Slide 9: OBD-II
Vehicle Network

## Slide 10: OBD-II
Vehicle Network
OBD-II
Data Link Connector

## Slide 11: OBD-II
Vehicle Network
Diagnostic
Scan Tool

## Slide 12: OBD-II
  Scan Tools.

## Slide 13: OBD-II
Vehicle Network
CAN Bus

## Slide 14: CAN
Controller Area Network.
  Bus allowing communications between ECU’s inside the vehicle.
  Message Based Protocol (Frame).
  Carrier Sense Multiple Access with Collision Avoidance (CSMA/CA).
  Not only communications protocol implemented in vehicles (cf LIN, MOST) but most common.
https://en.wikipedia.org/wiki/CAN_bus

## Slide 15: OBD-II
Vehicle Network

## Slide 16: Security Issues

## Slide 17: Security Issues
’CAN, by design, offers no protection from manipulation’
(Miller, 2013), (Koscher, 2010)
No source address => No certainty about origin.
Broadcast nature => Information Disclosure.
Prioritized ID’s => Denial of Service.
No support for encryption or authentication.

## Slide 18: Security Issues
Potential hacking results.
  Vehicle Theft.
  Changing Emission information (“Dieselgate”).
  Reduce odometer value.
  Change recorded data after crash.
  …
EXTREMETECH, „Hack the diagnostics connector, steal yourself a BMW in 3 minutes
Stephanie Bayer, Thomas Enderle, Dennis Kengo Oka , Marko Wolf .
Security Crash Test – Practical Security Evaluations of Automotive Onboard IT Components

## Slide 19: Threat Model
Vehicle Network
Physical Access to OBD-II DLC.
Ability to inject arbitrary packets.
Able to exploit vulnerabilities in ECU software.
Enable wireless connectivity.

## Slide 20: Proposed Solution: OBD-II Role Based Access Control

## Slide 21: Solution
Proposed solution: Role Based Access Control.
Every role determines what kind of access is permitted.
For example:
  Repair shop => Read diagnostics information only.
  Official dealership => Diagnostics + ability to fix/test faulty ECU’s.
  Police => Check integrity of vehicle network.

## Slide 22: Solution
Central gateway (CGW).
  Acts as router for all subnetworks + gate for all incoming data.
Perfect place to implement access control solution.

## Slide 23: Solution
Vehicle Network
Private Key
Public Key
Central Gateway

## Slide 24: Solution
Implementation:
  Microcontroller with CAN controller (AT90CAN128).
  CAN Transceiver.
  OBD-II connector.
Demo:
  CAN testbench designed at KuLeuven for testing VulCAN.
Jo Van Bulck, Jan Tobias Mühlberg, and Frank Piessens
December 2017

## Slide 25: Planning Next Three Months

## Slide 26: Planning
December:
  Get Familiar with Microcontroller software development.
  Write December paper/poster.
January & February:
  Implement a simple CAN compliant device.
  Start Implementing rudimentary access control.

## Slide 27: Questions? Notes: - Timing.

## Slide 28
Timing difficulties.
Major Challenges!: Key infrastructure, Key size, …
No Slowing Down!!!

## Slide 29: CAN Protocol

## Slide 30: CAN
Controller Area Network.
  Bus allowing communications between ECU’s inside the vehicle.
  Message Based Protocol.
  Carrier Sense Multiple Access with Collision Avoidance (CSMA/CA).
  Not only communications protocol implemented in vehicles (cf LIN, MOST) but most common.

## Slide 31: CAN Frame
Identity Field
  Used to identify each ECU in the vehicle.
  Also specifies a priority (Lowest ID = highest priority).
  Bitwise contention resolution (1 = Recessive & 0 = Dominant).
Name | SOF | ID | RTR | IDE | r0 | DLC | Data | CRC | CRCd | ACK | EOF
No. Bits | 1 | 11 | 1 | 1 | 1 | 4 | 64 | 15 | 1 | 2 | 7

## Slide 32: CAN Bitwise Contention Resolution
1 | 1 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0
0 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0
Node 1
Node 2
Node 3
Node 4
Value Transmitted: 0

## Slide 33: CAN Bitwise Contention Resolution
1 | 1 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0
0 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0
Node 1
Node 2
Node 3
Node 4
Value Transmitted: 0

## Slide 34: CAN Bitwise Contention Resolution
1 | 1 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0
0 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0
Node 1
Node 2
Node 3
Node 4
Value Transmitted: 0

## Slide 35: CAN Bitwise Contention Resolution
1 | 1 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0
0 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0
Node 1
Node 2
Node 3
Node 4
Value Transmitted: 1

## Slide 36: CAN Frame
Data Field
  Carries the payload.
  Length is 64 so only 8 bytes of data in each message.
Name | SOF | ID | RTR | IDE | r0 | DLC | Data | CRC | CRCd | ACK | EOF
No. Bits | 1 | 11 | 1 | 1 | 1 | 4 | 64 | 15 | 1 | 2 | 7

## Slide 37: OBD-II

## Slide 38: OBD-II
Parameter ID’s (PID)
  Codes to request data from a vehicle.
  Typical Use (with scan tool connected to DLC):
    Technician enters PID on the scan tool.
    PID is sent to the CAN bus (accessed via the DLC).
    Some ECU recognises the PID and reports the corresponding value on the bus.
    Scan tool reads response and displays it to the technician.

## Slide 39: Security Issues
Potential hacking results (safety critical).
  Driver Distractions (wipers etc.).
  Engine shutoff.
  Steering changes.
  …

## Slide 40: Physical Access
Impossible to completely deny physical access.
Solutions rely on reducing potential harm of unauthorized access:
  Seed-key mechanism
  Two-way authentication between ECU’s.
  Timer method.
  Intrusion detection system.
  Honeypot.
  VulCAN.

## Slide 41: Bluetooth
Standard Bluetooth security not sufficient.
Large protocol stack, so susceptible to multiple attacks:
  Cipher attacks, Bluejacking, Backdoor attack, etc.
Solutions should apply to the Bluetooth implementation used inside the vehicle.

## Slide 42: Remote Keyless Entry
Most cars today use RF-based remote keyless entry (RKE)
radio transmitter sends encrypted data containing identifying information.
The ECU can determine if the key is valid and lock, unlock, and start the vehicle

## Slide 43: Tire Pressure Monitoring System
Each tire has pressure sensor.
Transmits real time data to an ECU.
Radio signal can be blocked/mimicked.
  Solution: ?

## Slide 44: Distributed Software

## Slide 45: Secure Software & Systems