## Slide 1: Security in Automobiles: Vulnerability and Protection of the on-board diagnostics port (OBD-II)
Michiel Willems, 01/02/19
Master of Engineering: Computer Science (Secure software)
Promotor: prof.dr. Bruno Cripso, Assistants: Mahmoud Ammar & Hassaan Janjua
Assesors: Dr. J.T. Mühlberg & Prof. dr. D. Weyns

## Slide 2: Outline
Introduction
Background
Securing the OBD-II port
Implementation
Evaluation
Conclusion
Notes: Pretty much follows thesis structure.
No verbal summation (not a fan)

## Slide 3: Introduction

## Slide 4: Introduction – Context
https://www.telematicswire.net/articles_interviews_qa-2/articles_inhouse_invited/cybersecurity-a-gating-issue-for-safety-in-a-connected-and-automated-vehicle-future/
Notes: Automobile hacking major concerns of software security.
100Milion lines of code, spread out over 70 ECU’s
ECU’s connected via networking protocols (i.e. CAN).
Increased connectability = More attack surfaces
Some example attack surfaces:
- Bluetooth (Bluetooth large protocol stack, lots of vulnerabilities).
- Tire Pressure Monitoring System: transmit false packets.
- OBD-II is one of these attack surfaces.

## Slide 5: Introduction – Problem Statement
On-Board Diagnostics (OBD-II)
  Help technicians diagnose and repair complex problems
  Allows access to vehicle subsystems via connector.
  Works with multiple signalling protocols (CAN mostly used).
https://en.wikipedia.org/wiki/On-board_diagnostics
Allen Lyons, California Air Resources Board , On-Board Diagnostics (OBD) Program Overview, 2015 .
Notes: 1996: The OBD-II specification is made mandatory for all cars manufactured in the United States to be sold in the United States.

## Slide 6: Introduction – Problem Statement
Intra Vehicle Network
Central Gateway
Sub-Networks
User
CAN
Notes: Normal situation: User connects to internal network via OBD-II DLC to retrieve diagnostics info.
Dangerous situation: User replaced by attacker, gaining easy access to internal network, injecting arbitrary messages.
These messages could trick systems into performing certain actions erroneously.

## Slide 7: Challenges
Compatibility
  portability, practicality, no hardware modifications.
Performance
  Speed, no interference with other systems.
Security
  Protect against unauthorised access.

## Slide 8: Contribution
The proposal of a role-based access control model for OBD-II, based on public-key cryptography.
Provide open source ‘proof-of-concept’ implementation on resource-constrained hardware and evaluate based on proposed challenges.

## Slide 9: Background

## Slide 10: Background – Intra vehicle networks
Cyber security and resilience of smart cars. Technical report, Agency for Network and Information Security (ENISA), 2016.
Notes: Typical intra vehicle network consists of multiple sub-networks with different responsebilities.
Each sub-network uses a distinct networking protocol that best suit its needs.
CAN is mostly used.
Key component = Gateway, performs signal mapping between different sub-networks + Handles incoming OBD-II transmissions.

## Slide 11: Background – CAN
Controller Area Network:
  Bus connecting ECU’s inside vehicle.
  Carrier Sense Multiple Access with Collision Avoidance (CSMA/CA)
  Identifier (ID) identifies content, not sender/receiver.
  ID also determines priority.
  No support for security.
ISO11898-1. Road vehicles – controller area network (can) – part 1: Data link layer and physical signalling. Technical report, International Organization for Standardization, 2015.
ISO11898-2: Road vehicles – controller area network (can) – part 2: High-speed medium access unit. Standard, International Organization for Standardization, 2016.
ISO11898-3: Road vehicles – controller area network (can) – part 3: Low- speed, fault-tolerant, medium-dependent interface. Standard, International Organization for Standardization, 2016.
Notes:   Eavesdropping
  No authentication
  No encryption
  Denial of service (DoS)

## Slide 12: Background – CAN
Frame formats:
ISO11898-1. Road vehicles – controller area network (can) – part 1: Data link layer and physical signalling. Technical report, International Organization for Standardization, 2015.
ISO11898-2: Road vehicles – controller area network (can) – part 2: High-speed medium access unit. Standard, International Organization for Standardization, 2016.
ISO11898-3: Road vehicles – controller area network (can) – part 3: Low- speed, fault-tolerant, medium-dependent interface. Standard, International Organization for Standardization, 2016.
Notes: 2 types: BASE type and Extended type.
Difference: extended has longer id (29 instead of 11)
Max Data of 8 bytes.

## Slide 13: Background – OBD-II
Data Link Connector (DLC).
Parameter ID’s (PID) to request data.
Diagnostic trouble codes (DTC) to identify faults.
Signalling protocols to handle communications (ISO-TP).
Hardware tools and adaptors.
ISO15031-5. Road vehicles – communication between vehicle and external equipment for emissions-related diagnostics – part 5: Emissions-related diagnostic services. Standard, International Organization for Standardization, 2015.
ISO15031-6. Road vehicles – communication between vehicle and external equipment for emissions-related diagnostics – part 6: Diagnostic trouble code definitions. Standard, International Organization for Standardization, 2015.
Wikipedia contributors. On-board diagnostics — Wikipedia, the free encyclopedia, 2018. [Online; accessed 29-November-2018]. URL: https://en.wikipedia. org/w/index.php?title=On-board_diagnostics&oldid=870086948.
Notes: DLC = 16pin connector with two types with different voltages
DTC’s comparable to Java Exceptions.
  Split message up into different CAN frames.
Hardware tools different types: standard OBD-II diagnostics tool, one with bluetooth/wifi compatability, one with USB connector.

## Slide 14: Background – OBD-II
Intra Vehicle Network
Central Gateway
Sub-Networks
User
ISO-TP
Diagnostic
scanning tool
DLC
Notes: Give example of how OBD-II works.

## Slide 15: Securing the OBD-II port

## Slide 16: Attacker Model
Type of Access:
  Physical Access:
  Session Hijacking:
Notes: Attacker Types:
  Targeting driver/passenger safety.
  Alteration by legitimate users.
  Surveillance.
  Theft.

## Slide 17: Securing the OBD-II port – Role Based Access Control
Intra Vehicle Network
Central Gateway
Sub-Networks
User
ISO-TP
OBD-II Server
Private keys
Internet
Connection
Public keys
Notes: OBD-II Role-based access control.
Each public/private key-pair associated with a specific role.
Each role will have permission to send a subset of messages (permission table)
Private keys stored on a obd-II server
Public keys stored on central gateway.
User first authenticates to the OBD-II server (e.g. login and password).
User will facilitate authentication to gateway by proving (s)he has access to OBD-II server (i.e. private key).

## Slide 18: Securing the OBD-II port
Notes: ECC because of it’s speed (optional: make comparison like 26 minutes (RSA DS) versus 6 seconds (ECDSA). Atmega328 microcontroller 16Mhz
Discuss procedure
Init message also contains role
Result: Central server authenticated to gateway. (i.e. use has access to central server).
Result: Both tester and gateway calculated shared secret.

## Slide 19: Securing the OBD-II port
Notes: Discuss procedure

## Slide 20: Securing the OBD-II port
Permission Table
Charlie Miller and Chris Valasek. Adventures in automotive networks and control units. 2014
Notes: Explain different roles: Admin, OEM, Repairman, Policeman, Owner
Examples (2010 Ford Escape):
0201: speedometer
0402: odometer
0000: DoS

## Slide 21: Implementation

## Slide 22: Implementation
Hardware: 2 x DVK90CAN1
  AT90CAN128 MCU (8 MHz)
  CAN Transceiver + Connector
  RS-232 driver/receiver + Connector
  Compass Card Keyboard
  Atmel-ICE Basic Programmer (JTAG)
http://ww1.microchip.com/downloads/en/devicedoc/doc4381.pdf
https://www.microchip.com/developmenttools/ProductDetails/atatmel-ice

## Slide 23: Implementation
Set-Up:
C Libraries:
  Micro-ECC for ECC, ECDSA and ECDH
  AVR-Crypto-Lib for SHA256, SHA512 and HMAC-SHA256
  ISOTP-C for ISO-TP
https://github.com/kmackay/micro-ecc
https://github.com/cantora/avr-crypto-lib
https://github.com/lishen2/isotp-c
Notes: OBD-II Server: Implemented on the tester (key API).
Intra vehicle network: RS232 connection with PC.
ECC because of it’s speed (make comparison like 26 minutes (RSA DS) versus 6 seconds (ECDSA). Atmega328 microcontroller 16Mhz
SHA-2 because they are more efficient than SHA-3 + more software libraries available

## Slide 24: Implementation
Scenario 1
Role: Owner

## Slide 25: Implementation
Scenario 2
Role: Owner

## Slide 26: Implementation
Scenario 3
Role: Admin

## Slide 27: Evaluation

## Slide 28: Evaluation
Compatibility:
  Program Memory:
  Flash Memory utilization: 22%
  RAM: 3 KB (ECC)
Notes: 32 KB is pessimistic estimate (ISO-TP, CAN, etc already implemented on gateway), CAN is about 4,5 KB.
Typical Program memory also within acceptable bounds.
Typical RAM up to several megabytes (so 3KB is ok) (Atmel, Infineon, ST).
Typical ECUs, has built-in hardware modules for ECC and SHA2, this means that the utilisation in real scenarios more or less will not exceed 1%.

## Slide 29: Evaluation
Performance:
  ECC operations take significant time
  Decoupling necessary
Notes: Most important procedures are the cryptographic ones, since each message takes only roughly 1.04 ms (online CAN speed calculator).
ECC operations very slow. Although modern gateways would have better performance + these operations can be implemented in hardware.
It is necessary to decouple OBD-II authentication and normal Gateway operation (i.e. signal mapping) to prevent system from shutting down (Dual processing, etc..)

## Slide 30: Evaluation
Security:
  Authentication
  Authorisation
  Replay Attack Resistant
  Integrity
  Confidentiality
  Side Channel Attack Resistant
Notes: Authentication: The user is authenticated in 2 steps: first to the OBD-Server (secure channel) + To the Gateway via the authentication procedure (ECDSA).
Once user disconnects: New authentication required. (Attacker would have to guess ECC private key or ECDSA signature).
Authorisation: OBD-II Server assigns roles to appropriate users + Permissions table enforces security policy.
Replay attacks: MAC prevents replay attacks (Generated public key is random -> secret also random) + Session timeouts.
Integrity: attacker would have to guess MAC/secret (this also holds for an attacker injecting their own messages).
Confidentiality: Private keys safely stored on OBD-II server. Session keys deleted when session ends.
Side channel attack: no secret data stored on gateway + session keys deleted.
Overall security is reduced to security of the cryptographic primitives: ECC and HMAC (guess private key, guess shared secret, guess signature, guess MAC).

## Slide 31: Conclusion

## Slide 32: Conclusion
Contribution in Review
  The proposal of a role-based access control model for OBD-II, based on public-key cryptography.
  Provide open source ‘proof-of-concept’ implementation on resource-constrained hardware and evaluate based on proposed challenges.
Future Work
  First step taken towards securing OBD-II.
Notes:   Future work OBD-II Roles, Permission Table, Central Server, Tester and OBD-II Applications

## Slide 33: Thank you!
Notes: Thanks to: My assistants, Bruno Crispo,

## Slide 34: Questions?

## Slide 35: XImplementation
Permission Table Implementation

## Slide 36: XImplementation
Notes: Discuss implementation(ISO-TP!!!)
Again MAC size to guarantee security level.

## Slide 37: XImplementation
Notes: Discuss implementation (everything is transmitted using ISO-TP!!!)
Security level of 128 bits.
Private/public key size to guarantee security level.
Signature size to guarantee security level.
Shared secret size to guarantee security level.

## Slide 38: XBackground – Software Security Preliminaries
Asymmetric key cryptography: ECC, ECDSA and ECDH.
Symmetric key cryptography: HMAC-SHA256.
Cryptographic Hash functions: SHA256 and SHA512.

## Slide 39: Background – CAN
Security Issues:
  Eavesdropping
  No authentication
  No encryption
  Denial of service (DoS)
Robert Buttigieg, Mario Farrugia, and Clyde Meli. Security issues in controller area networks in automobiles. Technical report, University of Malta, 2017.
Stephen Checkoway, Damon McCoy, Brian Kantor, Danny Anderson, Hovav Shacham, Stefan Savage, Karl Koscher, Alexei Czeskis, Franziska Roesner, and Tadayoshi Kohno.
Comprehensive experimental analyses of automotive attack surfaces. Technical report, University of California, San Diego and University of Washington.

## Slide 40: XBackground – Intra vehicle networks
Shane Tuhoy, Martin Glavin, Ciar ́an Hughes, Edward Jones, Mohan Trivedi, and Liam Kilmartin. Intra-vehicle networks: A review. IEEE Transactions on Intelligent Transportation Systems, January 2014.

## Slide 41: Evaluation
Security:
  Physical access attacks: ECDSA + Permission table + OBD-II Server
  Remote session hijacking: HMAC-SHA256.
  OBD-Server:
    Private key storage.
    Private key API.
    User Authentication.
  Cryptographic primitives.
Notes: Physical attacks: users are prevented from gaining unauthorised access via the OBD-II port because authentication is required first (AUTHENTICATION).
If access is granted, the permission table enforces a policy that is designed to limit access according to the user’s role (AUTHORISATION).
The OBD-II Server ensures that only authorised users are granted the ability to authenticate with the appropriate role.
Remote Session Hijacking: Tampering, replaying, etc is prevented by the use of the session key that changes frequently (HMAC_SAH256) (REPLAY ATTCK + INTEGRITY).
OBD-Server is in charge of safely storing the private keys (CONFIDENTIALITY) + Providing a safe private key api (signature generation + Shared secret establishment) + Secure user authentication (login + password).
Overall security is reduced to security of the cryptographic primitives: ECC and HMAC (guess private key, guess shared secret, guess signature, guess MAC).

## Slide 42: Attacker Model
Example Attacks:
Cyber security and resilience of smart cars. Technical report, Agency for Network and Information Security (ENISA), 2016.
Charlie Miller and Chris Valasek. Adventures in automotive networks and control units. 2014.
Notes: Attacker types + Example attacks

## Slide 43: Securing the OBD-II port
Example Attacks:
  Speedometer.
  Denial of Service.
  Diagnostic Session.
Charlie Miller and Chris Valasek. Adventures in automotive networks and control units. 2014.
Notes: Clicking shows multiple pictures.
Diagnostics session: explain seed key + weakness.

## Slide 44: Attacker Model – Remote Session Hijacking
Intra Vehicle Network
Central Gateway
Sub-Networks
User
CAN
Attacker

## Slide 45: Attacker Model – Physical Access
Intra Vehicle Network
Central Gateway
Sub-Networks
Attacker
CAN

## Slide 46: Background – OBD-II
OBD-II security issues:
  Provides direct access to intra vehicle network.
  Inherits security issues of underlying signalling protocol (i.e. CAN):
    Eavesdropping
    Denial of Service
    etc.

## Slide 47: Background – OBD-II
Signalling Protocol ISO 15765 CAN (ISO-TP).
  Speed: 250 or 500 kbit/sec.
  Message length up to 4095 bytes.
  Split message up into different CAN frames.
  First data byte = Protocol control information (PCI).
  4 types: Single (SF), First (FF), Consecutive (CF), Flow Control (FC).
ISO 15765-2:2016 Road vehicles -- Diagnostic communication over Controller Area Network (DoCAN) -- Part 2: Transport protocol and network layer services, Standard, Internation Organisation for standardization, 2016.
Notes: Mandatory in all vehicles since 2008.
Essentially every CAN message 7 bytes of data + 1 byte of PCI.

## Slide 48: Background – OBD-II
ISO-TP frame types:
  Single Frame (SF) = 0.
  First Frame (FF) = 1.
  Consecutive Frame (CF) = 2.
  Flow control Frame (FC) = 3.
ISO 15765-2:2016 Road vehicles -- Diagnostic communication over Controller Area Network (DoCAN) -- Part 2: Transport protocol and network layer services, Standard, Internation Organisation for standardization, 2016.

## Slide 49: Background – OBD-II
ISO-TP:
ISO 15765-2:2016 Road vehicles -- Diagnostic communication over Controller Area Network (DoCAN) -- Part 2: Transport protocol and network layer services, Standard, Internation Organisation for standardization, 2016.
Notes: Message longer than 7 bytes.
Consecutive frames until entire payload was delivered.

## Slide 50: Background – OBD-II
Data Link Connector (DLC)
ISO15031-3. Road vehicles – communication between vehicle and external equipment for emissions-related diagnostics – part 3: Diagnostic connector and related electrical circuits: Specification and use. Standard, International Organization for Standardization, 2016.
Wikipedia contributors. On-board diagnostics — Wikipedia, the free encyclopedia, 2018. [Online; accessed 29-November-2018]. URL: https://en.wikipedia. org/w/index.php?title=On-board_diagnostics&oldid=870086948.
Type A
Type B
Notes: Both are female connectors (found in vehicles)
law it is required to be installed within 0.61 m of the steering wheel
Type A uses 12V signal levels.
Type B uses 24V signal levels.
Design prevents insertion of type A male plug into a type B female socket

## Slide 51: Background – CAN
Message Arbitration:
  CAN ID bit either dominant (0) or recessive (1).
  Upon multiple concurrent transmission: arbitration.
  Lower ID = Higher priority.
ISO11898-1. Road vehicles – controller area network (can) – part 1: Data link layer and physical signalling. Technical report, International Organization for Standardization, 2015.
ISO11898-2: Road vehicles – controller area network (can) – part 2: High-speed medium access unit. Standard, International Organization for Standardization, 2016.
ISO11898-3: Road vehicles – controller area network (can) – part 3: Low- speed, fault-tolerant, medium-dependent interface. Standard, International Organization for Standardization, 2016.
Notes: Explain how message arbitration works.

## Slide 52: Background – CAN
Frames:
  Data frame
  Error frame
  Remote frame
  Overload frame
ISO11898-1. Road vehicles – controller area network (can) – part 1: Data link layer and physical signalling. Technical report, International Organization for Standardization, 2015.
ISO11898-2: Road vehicles – controller area network (can) – part 2: High-speed medium access unit. Standard, International Organization for Standardization, 2016.
ISO11898-3: Road vehicles – controller area network (can) – part 3: Low- speed, fault-tolerant, medium-dependent interface. Standard, International Organization for Standardization, 2016.
Notes: Explain goal of each frame type

## Slide 53: Background – CAN
Architecture:
Wikipedia contributors. Can bus — Wikipedia, the free encyclopedia, 2018. [Online; accessed 29-November-2018]. URL: https://en.wikipedia.org/w/ index.php?title=CAN_bus&oldid=870995924.
Notes: CAN Transceiver: implements physical layer.
CAN Controller: Transfer layer.
MCU: Object Layer + Application Layer.
CAN node = ECU

## Slide 54: Background – CAN
Layers:
  Application Layer.
  Object Layer.
  Transfer Layer.
  Physical Layer.
ISO11898-1. Road vehicles – controller area network (can) – part 1: Data link layer and physical signalling. Technical report, International Organization for Standardization, 2015.
ISO11898-2: Road vehicles – controller area network (can) – part 2: High-speed medium access unit. Standard, International Organization for Standardization, 2016.
ISO11898-3: Road vehicles – controller area network (can) – part 3: Low- speed, fault-tolerant, medium-dependent interface. Standard, International Organization for Standardization, 2016.
Notes: Explain general responsabilities of each layer.

## Slide 55: Introduction
Potential hacking results.
  Vehicle Theft.
  Changing Emission information (“Dieselgate”).
  Reduce odometer value.
  Change recorded data after crash.
  …
EXTREMETECH, „Hack the diagnostics connector, steal yourself a BMW in 3 minutes
Stephanie Bayer, Thomas Enderle, Dennis Kengo Oka , Marko Wolf .
Security Crash Test – Practical Security Evaluations of Automotive Onboard IT Components

## Slide 56: Introduction
Automobile hacking has become one of the major concerns for software security today:
  Over 100M lines of code deployed over more than 70 ECU’s.
  Networking protocols (e.g. CAN).
  Increasing connectability (Bluetooth, Wifi, etc).
Lee Pike, Jamey Sharp, Mark Tullsen, Patrick C. Hickey and James Bielman. 2015.
Securing the automobile: A comprehensive approach.
Dan Klinedinst, Christopher King. 2016
On Board Diagnostics: Risks and Vulnerabilities of the Connected Vehicle
Notes: Increasing connectability = Emergence of new attack surfaces.

## Slide 57
Survey vulnerabilities of the OBD-II interface.
The proposal of a role-based access control model for OBD-II, based on public-key cryptography.
Provide open source ‘proof-of-concept’ implementation on resource-constrained hardware and evaluate based on proposed challenges.

## Slide 58: Introduction
Automobile hacking has become one of the major concerns for software security today:
  Over 100M lines of code deployed over more than 70 ECU’s.
  Networking protocols (e.g. CAN).
  Increasing connectability (Bluetooth, Wifi, etc).
Lee Pike, Jamey Sharp, Mark Tullsen, Patrick C. Hickey and James Bielman. 2015.
Securing the automobile: A comprehensive approach.
Dan Klinedinst, Christopher King. 2016
On Board Diagnostics: Risks and Vulnerabilities of the Connected Vehicle

## Slide 59: OBD-II

## Slide 60: Security Issues
’CAN, by design, offers no protection from manipulation’
(Miller, 2013), (Koscher, 2010)
No source address => No certainty about origin.
Broadcast nature => Information Disclosure.
Prioritized ID’s => Denial of Service.
No support for encryption or authentication.

## Slide 61: Threat Model
Vehicle Network
Physical Access to OBD-II DLC.
Ability to inject arbitrary packets.
Able to exploit vulnerabilities in ECU software.

## Slide 62: OBD-II Access Control

## Slide 63: Introduction
Thesis Subject: Role Based Access Control.
Every role determines what kind of access is permitted.
For example:
  Repair shop => Read diagnostics information only.
  Official dealership => Diagnostics + ability to fix/test faulty ECU’s.
  Police => Check integrity of vehicle network.

## Slide 64: Introduction
Vehicle Network
Private Key
Public Key
Central Gateway

## Slide 65: Introduction
Challenges:
  PKI infrastructure.
  Authentication protocol (challenge response).
  Permissions table.
  Secure private key API.

## Slide 66: Security, Vulnerability and Protection of Vehicular On-board Diagnostics
Aastha Yadav, Gaurav Bose, Radhika Bhange, Karan Kapoor, N.Ch.S.N Iyengar, Ronnie D. Caytiles
VIT University.Vellore-632014, Tamilnadu, India, Hannam University, Korea

## Slide 67: Paper - Introduction
Outline:
  Introduction
  Motivation
  Background Research
  Points Entry
  On-Board Diagnostic (OBD)-II Port
  OBD-II Port Security Threats
  Security Solution
  Conclusion

## Slide 68: Paper - Introduction
Outline:
  Introduction
  Motivation
  Background Research
  Points Entry
  On-Board Diagnostic (OBD)-II Port
  OBD-II Port Security Threats
  Security Solution
  Conclusion

## Slide 69: Security, Vulnerability and Protection of Vehicular On-board Diagnostics
Aastha Yadav, Gaurav Bose, Radhika Bhange, Karan Kapoor, N.Ch.S.N Iyengar, Ronnie D. Caytiles
VIT University.Vellore-632014, Tamilnadu, India, Hannam University, Korea
Proposed Security Solutions

## Slide 70: Security Solutions – Seed Key Algorithm
Implement security at ECU level.
Every ECU holds a secret key.
Algorithm:
  Tester sends a PID to the ECU.
  ECU sends a seed value to the Tester.
  Both ECU and Tester calculate response from seed and secret key.
  Tester sends response to ECU where it is verified.

## Slide 71: Security Solutions – Seed Key Algorithm
Security Issues:
  Same secret key shared.
  Secret key stored in unprotected memory.
  Algorithms are proprietary and Confidential (Security through Obscurity).
  Seed values often too short ( 10 min to crack 16 bit seed ).
K. Koscher, A. Czeskis, F. Roesner, S. Patel, T. Kohno, S. Checkoway, D. McCoy, B. Kantor, D.Anderson and H.a.o. Shacham,
"Experimental security analysis of a modern automobile", Security and Privacy (SP), 2010 IEEE Symposium on, (2010).

## Slide 72: Security Solutions – Two Way Authentication
Extends Seed-Key Algorithm.
Introduce device that allows client (owner of car) to control access to the OBD-II port.
Device can be a pager, cell phone, smartphone app, bluetooth, etc.
Device allows client to receive and send acknowledgments.

## Slide 73: Security Solutions – Two Way Authentication

## Slide 74: Security Solutions – Timer Method
Extends Two-Way authentication method.
Introduces 2 things:
  Timer started once seed is received, if it runs out the client is notified.
  Client needs to enter code when completing acknowledgement.
Timer should prevent brute force attacks.

## Slide 75: Paper – My Issues
Solution assumes official tester device.
  Custom tester software could use revealed secret keys.
  Custom tester software would bypass two-way authentication.
Implementation uses small key and seed sizes.
  Demo uses 5 bit seeds and keys.
ECU is implemented only virtually (no CAN).

## Slide 76: Current Thesis Status

## Slide 77: Current Thesis Status
2 DVK90CAN1 AVR development boards (AT90CAN128).
Gateway:
  Holds public keys & permissions table.
Tester:
  Implements private key API.
  Authenticate & send OBD-II messages.

## Slide 78: Current Thesis Status
Authentication Request.
Tester
Gateway
Remote CAN frame
With Specific ID

## Slide 79: Current Thesis Status
Challenge
Tester
Gateway
2 CAN Frames
128 bit Challenge

## Slide 80: Current Thesis Status
Key Attestation
Tester
Gateway
8 CAN frames
512 bit Signature of Challenge

## Slide 81: Current Thesis Status
Elliptic Curve Digital Signature Algorithm.
Key Size:
  Security level is Key Size / 2 (smaller key than normal DSA).
  According to NSA 256 bit key sufficient (128-bit security level) .
Signature Size:
  Security level is Signature size / 4.
  A signature of size 512 bit will be sufficient (128-bit security level).
https://en.wikipedia.org/wiki/Key_size#cite_note-19
https://en.wikipedia.org/wiki/Elliptic_Curve_Digital_Signature_Algorithm

## Slide 82: Current Thesis Status
Authentication Request.
Tester
Gateway
Remote CAN frame
Acknowledgment

## Slide 83: Current Thesis Status
Send OBD-II message
Tester
Gateway
OBD-II message

## Slide 84: Current Thesis Status
Former protocol is for sending 1 OBD-II message.
If multiple messages are to be sent shared secret is established:
  Elliptic Curve Diffie-Hellman
Shared secret used as new symmetric key.
Every OBD-II message followed by MAC of message using shared symmetric key.
Periodically new symmetric key established.

## Slide 85: Current Thesis Status
Current Implementation:
  Relevant Microcontroller functions explored.
  2 AVR boards can send and receive CAN messages.
  Serial link between board and pc (for demo).
  Elliptic Curve Library (micro-ecc) imported and tested (Key Storage).
https://github.com/kmackay/micro-ecc

## Slide 86: Planning next 2 months

## Slide 87: Planning
Implementation:
  Finish Authentication + ECDH protocol.
  Build permissions table.
  Tester private key API.
    represents online API for interacting with private keys.
    This API should be secure!
Testing.

## Slide 88: Planning
Writing:
  Finishing touches: Literary Review, Background (CAN & OBD-II), Contributions, Introduction and Abstract.
  OBD-II Access control (explanation of implemented protocol).
  Formulation and interpretation of test results.
  Conclusion.

## Slide 89: Questions?

## Slide 90: OBD-II
On Board Diagnostics Protocol.
  Help Technicians Diagnose and Repair Complex Problems
  Allows access to vehicle subsystems via connector.
  Introduces parameter ID’s (PID) to request data from ECU’s.
  PID manufacturer and model specific.
  Works with multiple signalling protocols, but CAN mostly used.
https://en.wikipedia.org/wiki/On-board_diagnostics

## Slide 91: OBD-II
Vehicle Network

## Slide 92: OBD-II
Vehicle Network
OBD-II
Data Link Connector

## Slide 93: OBD-II
Vehicle Network
Diagnostic
Scan Tool

## Slide 94: OBD-II
  Scan Tools.

## Slide 95: OBD-II
Vehicle Network
CAN Bus

## Slide 96: CAN
Controller Area Network.
  Bus allowing communications between ECU’s inside the vehicle.
  Message Based Protocol (Frame).
  Carrier Sense Multiple Access with Collision Avoidance (CSMA/CA).
  Not only communications protocol implemented in vehicles (cf LIN, MOST) but most common.
https://en.wikipedia.org/wiki/CAN_bus

## Slide 97: OBD-II
Vehicle Network

## Slide 98: Security Issues

## Slide 99: Security Issues
’CAN, by design, offers no protection from manipulation’
(Miller, 2013), (Koscher, 2010)
No source address => No certainty about origin.
Broadcast nature => Information Disclosure.
Prioritized ID’s => Denial of Service.
No support for encryption or authentication.

## Slide 100: Threat Model
Vehicle Network
Physical Access to OBD-II DLC.
Ability to inject arbitrary packets.
Able to exploit vulnerabilities in ECU software.
Enable wireless connectivity.

## Slide 101: Proposed Solution: OBD-II Role Based Access Control

## Slide 102: Solution
Proposed solution: Role Based Access Control.
Every role determines what kind of access is permitted.
For example:
  Repair shop => Read diagnostics information only.
  Official dealership => Diagnostics + ability to fix/test faulty ECU’s.
  Police => Check integrity of vehicle network.

## Slide 103: Solution
Central gateway (CGW).
  Acts as router for all subnetworks + gate for all incoming data.
Perfect place to implement access control solution.

## Slide 104
Intra Vehicle Network
Central Gateway
Sub-Networks
User
CAN
Central Server
Private keys
Internet
Connection
Public Key

## Slide 105: Solution
Intra Vehicle Network
Central Gateway
Sub-Networks
User
CAN
Attacker

## Slide 106: Solution
Intra Vehicle Network
Central Gateway
Sub-Networks
Attacker
CAN

## Slide 107: Solution
Implementation:
  Microcontroller with CAN controller (AT90CAN128).
  CAN Transceiver.
  OBD-II connector.
Demo:
  CAN testbench designed at KuLeuven for testing VulCAN.
Jo Van Bulck, Jan Tobias Mühlberg, and Frank Piessens
December 2017

## Slide 108: Planning Next Three Months

## Slide 109: Planning
December:
  Get Familiar with Microcontroller software development.
  Write December paper/poster.
January & February:
  Implement a simple CAN compliant device.
  Start Implementing rudimentary access control.

## Slide 110: Questions? Notes: - Timing.

## Slide 111
Timing difficulties.
Major Challenges!: Key infrastructure, Key size, …
No Slowing Down!!!

## Slide 112: CAN Protocol

## Slide 113: CAN
Controller Area Network.
  Bus allowing communications between ECU’s inside the vehicle.
  Message Based Protocol.
  Carrier Sense Multiple Access with Collision Avoidance (CSMA/CA).
  Not only communications protocol implemented in vehicles (cf LIN, MOST) but most common.

## Slide 114: CAN Frame
Identity Field
  Used to identify each ECU in the vehicle.
  Also specifies a priority (Lowest ID = highest priority).
  Bitwise contention resolution (1 = Recessive & 0 = Dominant).
Name | SOF | ID | RTR | IDE | r0 | DLC | Data | CRC | CRCd | ACK | EOF
No. Bits | 1 | 11 | 1 | 1 | 1 | 4 | 64 | 15 | 1 | 2 | 7

## Slide 115: CAN Bitwise Contention Resolution
1 | 1 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0
0 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0
Node 1
Node 2
Node 3
Node 4
Value Transmitted: 0

## Slide 116: CAN Bitwise Contention Resolution
1 | 1 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0
0 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0
Node 1
Node 2
Node 3
Node 4
Value Transmitted: 0

## Slide 117: CAN Bitwise Contention Resolution
1 | 1 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0
0 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0
Node 1
Node 2
Node 3
Node 4
Value Transmitted: 0

## Slide 118: CAN Bitwise Contention Resolution
1 | 1 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0
0 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0
Node 1
Node 2
Node 3
Node 4
Value Transmitted: 1

## Slide 119: CAN Frame
Data Field
  Carries the payload.
  Length is 64 so only 8 bytes of data in each message.
Name | SOF | ID | RTR | IDE | r0 | DLC | Data | CRC | CRCd | ACK | EOF
No. Bits | 1 | 11 | 1 | 1 | 1 | 4 | 64 | 15 | 1 | 2 | 7

## Slide 120: OBD-II

## Slide 121: OBD-II
Parameter ID’s (PID)
  Codes to request data from a vehicle.
  Typical Use (with scan tool connected to DLC):
    Technician enters PID on the scan tool.
    PID is sent to the CAN bus (accessed via the DLC).
    Some ECU recognises the PID and reports the corresponding value on the bus.
    Scan tool reads response and displays it to the technician.

## Slide 122: OBD-II
Parameter ID’s (PID)
  Codes to request data from a vehicle.
  Typical Use (with scan tool connected to DLC):
    Technician enters PID on the scan tool.
    PID is sent to the CAN bus (accessed via the DLC).
    Some ECU recognises the PID and reports the corresponding value on the bus.
    Scan tool reads response and displays it to the technician.

## Slide 123: Security Issues
Potential hacking results (safety critical).
  Driver Distractions (wipers etc.).
  Engine shutoff.
  Steering changes.
  …

## Slide 124: Physical Access
Impossible to completely deny physical access.
Solutions rely on reducing potential harm of unauthorized access:
  Seed-key mechanism
  Two-way authentication between ECU’s.
  Timer method.
  Intrusion detection system.
  Honeypot.
  VulCAN.

## Slide 125: Bluetooth
Standard Bluetooth security not sufficient.
Large protocol stack, so susceptible to multiple attacks:
  Cipher attacks, Bluejacking, Backdoor attack, etc.
Solutions should apply to the Bluetooth implementation used inside the vehicle.

## Slide 126: Remote Keyless Entry
Most cars today use RF-based remote keyless entry (RKE)
radio transmitter sends encrypted data containing identifying information.
The ECU can determine if the key is valid and lock, unlock, and start the vehicle

## Slide 127: Tire Pressure Monitoring System
Each tire has pressure sensor.
Transmits real time data to an ECU.
Radio signal can be blocked/mimicked.
  Solution: ?

## Slide 128: Distributed Software

## Slide 129: Secure Software & Systems